UPDATE No. 3

November 1, 2016

TENDER

TO SUPPLY ALL LABOUR, EQUIPMENT AND MATERIALS FOR THE FABRICATION OF WALLS AND STRUCTURES, SHOWCASES AND GRAPHIC PANELS OF THE NEW ARCTIC GALLERY OF THE

CANADIAN MUSEUM OF NATURE

Ref. # 16-1630-CMN-069

CLOSING DATE

Monday, November 28, 2016 @ 3 PM

The Canadian Museum of Nature (CMN) has received questions regarding the above noted Tender.  A written reply to the questions is provided.

Question 8:

Item ''Z06-400 The web''

In the GSM plans, there is no way to calculate the length of steel cable and acrylic tubing to be glued on the walls. Can you provide us with quantities?

Answer 8:

Approximately 375 m. or 1230’ 4’’

Question 9:

In the technical specifications of the tender notice, point 6.8 regarding the Showcases, paragraph 2, it is written that: The glass making up the showcases must be tempered, with the thickness and lamination to be validated with the “showcase” Contractor and the CMN.

We believe that there is some confusion here, and we would like that a precise specification for the glass be published because it greatly influences the costs for the showcases. We understand that the thickness of the glass could vary according to the manufacturing method and the type of glass bonding.

Glass can be tempered only, laminated only, or tempered-laminated, all in two composition options: regular glass and so-called “ultra-white” glass, with low iron content. Costs for the glass used in the manufacturing of the showcases will vary considerably with the type of glass used, and the specification for the type of glass should therefore be detailed in order to get comparable propositions.

It goes without saying that showcases made of regular tempered glass will have a manufacturing cost that is lower than those made of laminated ultra-white glass.

The reason for this is that the layers of the pieces of tempered-laminated glass are difficult to buff during manufacturing in order to get a perfectly smooth surface, contrary to the two other types (tempered or laminated) which could be used.

Answer 9:

Glass specifications:

-        6 to 8 mm thick tempered glass, depending on the size of the showcase.

Manufacturing technique for zone display:

-        Digital cutting and buffing

-        3 to 8 mm thick silicone gasket, depending on the dimensions of the pieces of glass

-        The wooden casing required for positioning of the lighting must have a steel base

with an airtight back panel